실습 5 : JK F/F 과 시프트 레지스터 2008-5-22-목

(1) JK Flip Flop

LIBRARY IEEE; USE IEEE.STD_LOGIC_1164.ALL; ENTITY EX_5_2_V IS PORT( CLK, J, K, PRN, CLR : IN BIT; Q : BUFFER BIT; QN : OUT BIT); END EX_5_2_V; ARCHITECTURE BH OF EX_5_2_V IS BEGIN PROCESS(CLK, PRN, CLR) BEGIN IF PRN = '0' THEN Q <= '1'; QN <= '0'; ELSIF CLR = '0' THEN Q <= '0'; QN <= '1'; ELSIF CLK'EVENT AND CLK = '1' THEN IF J = '1' AND K = '0' THEN Q <= '1'; QN <= '0'; ELSIF J = '0' AND K = '1' THEN Q <= '0'; QN <= '1'; ELSIF J = '1' AND K = '1' THEN Q <= NOT Q; QN <= Q; END IF; END IF; END PROCESS; END BH;

| 입 력 | 출 력 |
| --- | --- |
| 핀이름 | 연결소자 | ALTERA | 핀이름 | 연결소자 | ALTERA |
| PRN | SW0 | Y13 | Q | LED1 | AF7 |
| CLR | SW1 | AB12 | QN | LED2 | AE7 |
| (S)J | SW_1 | Y10 |  |  |  |
| (R)K | SW_2 | W10 |  |  |  |
| CLK | SW_3 | AA9 |  |  |  |

<핀설정>

| 입 력 | 출 력 |
| --- | --- |
| CLR | PR | CK | J | K | Q | QN |
| 0 | 1 | X | X | X |  |  |
| 1 | 0 | X | X | X |  |  |
| 1 | 1 | ↑ | 0 | 0 |  |  |
|  |  | ↑ | 0 | 1 |  |  |
|  |  | ↑ | 1 | 0 |  |  |
|  |  | ↑ | 1 | 1 |  |  |

<결과확인>

(2) 8비트 시프트 레지스터

EX_5_3_V.vhd

LIBRARY IEEE; USE IEEE.STD_LOGIC_1164.ALL; ENTITY EX_5_3_V IS PORT( RST, SI, CLK : IN STD_LOGIC; REG : OUT STD_LOGIC_VECTOR(7 DOWNTO 0)); END EX_5_3_V; ARCHITECTURE BF OF EX_5_3_V IS SIGNAL SR : STD_LOGIC_VECTOR(7 DOWNTO 0); COMPONENT DIFF_RST PORT( D, RST, CLK : IN STD_LOGIC; Q : OUT STD_LOGIC); END COMPONENT; BEGIN DF7 : DIFF_RST PORT MAP(SI, RST, CLK, SR(7)); DF6 : DIFF_RST PORT MAP(SR(7), RST, CLK, SR(6)); DF5 : DIFF_RST PORT MAP(SR(6), RST, CLK, SR(5)); DF4 : DIFF_RST PORT MAP(SR(5), RST, CLK, SR(4)); DF3 : DIFF_RST PORT MAP(SR(4), RST, CLK, SR(3)); DF2 : DIFF_RST PORT MAP(SR(3), RST, CLK, SR(2)); DF1 : DIFF_RST PORT MAP(SR(2), RST, CLK, SR(1)); DF0 : DIFF_RST PORT MAP(SR(1), RST, CLK, SR(0)); REG <= SR; END BF;

DIFF_RST.vhd

LIBRARY IEEE; USE IEEE.STD_LOGIC_1164.ALL; ENTITY DIFF_RST IS PORT( D, RST, CLK : IN STD_LOGIC; Q : OUT STD_LOGIC); END DIFF_RST; ARCHITECTURE BF OF DIFF_RST IS BEGIN PROCESS(RST, CLK) BEGIN IF RST = '0' THEN Q <= '0'; ELSIF (CLK'EVENT AND CLK = '1') THEN Q <= D; END IF; END PROCESS; END BF;

| 입력 | 출력 |
| --- | --- |
| 핀이름 | 연결소자 | ALTERA | 핀이름 | 연결소자 | ALTERA |
| RST | SW8 | Y13 | REG[7] | LED1 | AF7 |
| SI | SW_1 | Y10 | REG[6] | LED2 | AE7 |
| CLK | SW_2 | W10 | REG[5] | LED3 | AB8 |
|  |  |  | REG[4] | LED4 | W8 |
|  |  |  | REG[3] | LED5 | AF6 |
|  |  |  | REG[2] | LED6 | AE6 |
|  |  |  | REG[1] | LED7 | AD7 |
|  |  |  | REG[0] | LED8 | AC7 |

<핀설정>